## Slide 1: HOS UDW2P Converter
NWT JIP
Xu Haihua, Harrif Santo, Law Yun Zhi, Prof. Allan Magee
Technology Centre for Offshore and Marine, Singapore
Notes: The data are solved in folder: D:\WP1\potentialFlowCompare
The python scripts are:
1 - Compare_Regular_Wave_v2.ipynb
2 - Compare_Irregular_Wave.ipynb

## Slide 2: Sketch of Domain for HOS and UDW2P
HOS Left BC
(Periodic)
HOS Right BC
(Periodic)
Wave From right BC
Wave to left BC
UDW2P Left BC
(xmin)
UDW2P Right BC
(xmax)
UDW2P Domain
HOS Domain
: HOS Domain
: UDW2P
Fig 1. Sketch of Domain for HOS and UDW2P
Function:
  The HOS UDW2P Converter converts the HOS results to UDW2P file format to carry out the potential flow and CFD coupling.
Program
  Program name: HOS2UDW2P_Converter.exe
  input file: input_converter.dat, modes_HOS_SWENSE.dat
  output file: PNWT.rec
Data Unit normalized by water depth and gravity
  Length: normalized by water depth
  Time: normalized by
  Grid size : normalized by
  Surface elevation :normalized by
  Velocity, : normalized by

## Slide 3: “input_converter.dat”
Variable | Meaning | Remarks
xmin | Minimum x in UDW2P domain, unit is m. | Shown in Fig 1 (only works for iHOS=1)
xmax | Minimum x in UDW2P domain, unit is m. | Shown in fig 1 (only works for iHOS=1)
nx | Number of x axis grid points in UDW2p domain | Distance between two grid points ((only works for iHOS=1)
nz | Number of sigma layer in UDW2p domain. nz=20 in current version. | Number of sigma layers in UDW2P domain. Point location is Gauss quadrature sampling points.
tStart | Start time to extract from HOS results, unit is second. | HOS time always start from t=0.
tEnd | End time to extract from HOS results, unit is second | End time must not larger than HOS output time.
iHOS | Type of HOS model. | HOS Ocean model iHOS=1 HOS NWT model iHOS =2
fileName | HOS results file path | The HOS SWENSE file path
iOMPCores | Number of Cores of OpenMP parallel | Suggest value is equal to the number of cores in the computer
iDebug | =1 Output ASICII file for debug the results. | Output file: Debug_LF_*.dat, Debug_RF_*.dat and Debug_SF_*.dat
Variable | Meaning | Remarks
xmin | Minimum x in UDW2P domain, unit is m. | Shown in Fig 1 (only works for iHOS=1)
xmax | Minimum x in UDW2P domain, unit is m. | Shown in fig 1 (only works for iHOS=1)
nx | Number of x axis grid points in UDW2p domain | 
nz | Number of sigma layer in UDW2p domain. nz=20 in current version. | 
tStart | Start time to extract from HOS results, unit is second. | HOS time always start from t=0.
tEnd | End time to extract from HOS results, unit is second | End time must not larger than HOS output time.
iHOS | Type of HOS model. | HOS Ocean model iHOS=1 HOS NWT model iHOS =2
fileName | HOS results file path | The HOS SWENSE file path
iOMPCores | Number of Cores of OpenMP parallel | Suggest value is equal to the number of cores in the computer
iDebug | =1 Output ASICII file for debug the results. | Output file: Debug_LF_*.dat, Debug_RF_*.dat and Debug_SF_*.dat

## Slide 4: “PNWT.rec” file format
Reference from NWT JIP
ASCII data
xScale is water depth , hence WD=h is 1
tScale =
xCalib unknown, set to 0
Binary data
Binary data in each record is :
Free surface elevation
Free surface elevation time derivative
Left side boundary
Right side boundary
Related Fortran subroutine
Software change to HOS

## Slide 5: Debug file data
Debug_SF_*.dat: free surface data
  * is record number
  output data ：
Debug_LF_*.dat: left side BC data:
  * is record number
  output data：
Debug_RF_*.dat: right side BC data
  * is record number
  output data：

## Slide 6: Benchmark data
Case | Case #2
Wave Height H (m) | 0.05
Depth D (m) | 1
Wave Length λ (m) | 1
Wave Period T (s) | 0.79049
Wave steepness H/λ | 5%
Domain Length L (m) | 60m
Simulation Time | 80s
Wave Parameters
HOS Left BC
(Periodic)
HOS Right BC
(Periodic)
Wave From right BC
Wave to left BC
UDW2P Domain
HOS Domain
L=60m
H=1.0m

## Slide 7: Compare with at T=20s
The two results are very close, which means is correct